Secondary Storage

Magnetic storage:
- works by magnetising parts of a substance
- north/south poles represent 0 and 1 respectively
- a hard drive platter is made of aluminium or glass, with a very thin coating of a magnetic material

Optical storage:
- uses light to shine a surface
- reflected light represents 1 in binary, no reflection represents 0
- CDs, DVDs are optical media

Types of optical media:
ROM media
  - data is pre-written
  - cannot be overwritten
  - used for music, films, games
R
  - blank
  - can be written only once
RW
  - readable, writeable more than once

Solid-state storage:
- also known as flash storage
- transistors are used to hold data
- unlike RAM (which is also a form of flash storage), SSDs are non-volatile

Comparison table:

Medium	Type	Capacity	Speed	Portability	Durability	Reliability
Hard disk	Magnetic	500 GB - / 12 TB	Slow	Internal devices are fixed. External drives are portable.	Prone to damage if dropped/knocked	Reliable if looked after
CD-ROM/R	Optical	670 MB	Slow	Very portable	Easily scratched, damaged	Reliable if looked after
CD-RW
DVD-ROM/R		4.7 GB
DVD-RW
SSD	Flash	250 GB - / 4 TB	Very fast	Internal devices are fixed. External drives are portable.	Robust and resilient	Reliable